How do I copy the Instrument ID from my Tyros3 or Tyros4?

Please follow these steps:

- Insert a compatible USB storage device into your instrument.

- While holding down DIRECT ACCESS, press EXPANSION to reach the Owner Screen.

- Press [I] to export the Instrument ID.

- Press [G] to copy Instrument ID to your USB storage device.

- When copy is complete, press [F].

- Remove the USB Storage device from your instrument and bring it to your computer.

You should be able to see a file called "instrument_id.n26" on your USB storage device. If you do not, please confirm you are using a compatible USB storage device. If you are still unable to create an instrument ID, please contact us for assistance.

How do I copy a Tyros3 or Tyros4 license key and/or voice from my computer to USB storage device?

Please follow these steps:

- Download the license key and/or voice file(s).

- Once your download is complete, copy the unzipped voice file(s) and the license key to your USB storage device by using the "copy and paste" or "drag and drop" features on your computer.

- Do not rename the files. Do not take the files out of the folder they came in.

How do I import a license key or load a voice to a Tyros4 using a USB storage device?

Please follow these steps:

- Insert your USB storage device containing your license key or voice into the USB port on your instrument (located just to the right of the keyboard).

- To import the license key, press and hold [DIRECT ACCESS], and then press [EXPANSION] to display the Owner Screen.

- Press [J], then [G] to import the License Key.

- When importing is complete, the upper portion of the OWNER page will display the message: License Key: REGISTERED

- Press [G] to confirm installation.

- Your instrument is now licensed. You may skip this step next time you load a Voice on this instrument.

- Now, let's load the Voice. If you are loading more than one Voice pack, you will need to repeat the following steps for each pack.

- Press [FUNCTION] on your instrument. (located under Menu, to the right of the center screen)

- Press [J]. Your Tyros will now display the Pack screen.

- Select the desired folder of the Pack or Voice you wan to install by pressing the button next to it one time.

- Press [F] to continue.

- Press [G] to install the pack. Do not disconnect your USB storage device from the instrument. You must leave it connected to use your instrument. It may take a few minutes to complete the loading process. Once installation is complete, press [G].

How do I import a license key or load a voice to the Tyros3 using a USB storage device?

Please follow these steps:

- Insert your USB storage device containing your license key or voice into the USB port on your instrument (located just to the right of the keyboard).

- To import the license key, press and hold [DIRECT ACCESS], and then press [EXPANSION] to display the Owner Screen.

- Press [J], then [G] to import the License Key.

- When importing is complete, the upper portion of the OWNER page will display the message: License Key: REGISTERED

- Press [G] to confirm installation.

- Your instrument is now licensed. You may skip this step next time you load a Voice on this instrument.

- Now, let's load the Voice. If you are loading more than one Voice pack, you will need to repeat the following steps for each pack.

- Press [VOICE CREATOR] on your instrument. (located under Menu, to the right of the center screen)

- Press [A]. Your Tyros will now display the Library Load screen.

- Select the desired voice by pressing the button next to the filename you wish to load. (If your USB storage device is not displayed, use the TAB buttons to select it.)

- Press [G] to load the file.

- Do not disconnect your USB storage device from the instrument. You must leave it connected to use your voice

How can I re-download my purchased Tyros3 or Tyros4 Premium Packs and Voices?

Please access the Redownload Items page in My Acccount. Then, you will see the "DOWNLOAD" button for your puchased item.

How can I reload purchased Voice Data to a new/replaced Tyros3 or Tyros4?

Please contact Yamaha MusicSoft customer support and ask them to remove the registered License Key associated with your old instrument so that you can create a new License Key for your new instrument. (Your old instrument will no longer be able to use the purchased voice.)

How can I reload purchased Voice Data to a new/replaced Tyros3 or Tyros4?

Please contact Yamaha MusicSoft customer support and ask them to remove the registered License Key associated with your old instrument so that you can create a new License Key for your new instrument. (Your old instrument will no longer be able to use the purchased voice.)

How do I load voices on my Tyros3 using the optional USB cable method?

To load a Voice to your instrument using a USB cable, follow these steps.

Note: The advantage of loading a Voice using this method is that you do not need to keep a USB storage device connected to your instrument to use the Voice.

Special Requirements:

- You have already imported your License Key to your instrument

- USB cable

- Connect a USB 2.0 cable between your computer and the instrument.

- Restart instrument in hard-disk mode by pressing [MUSIC FINDER] (located just to the right of the instrument's screen) while starting up the instrument. See P. 97 of Owner's Manual for details.

- Open "TYROS3_HD" (hard drive) from your computer and copy the unzipped Voice files from your computer to the instrument. Do not rename the files. Do not take the files out of the folder they came in.

- Once copying is complete, go to the next step.

- Restart the instrument by pressing [EXIT] (located under Menu, near the bottom right corner of the screen). You may now load the Voice.

- Now, let's load the Voice. If you are loading more than one Voice pack, you will need to repeat the following steps for each pack.

- Press [VOICE CREATOR] on your instrument (located under Menu, to the right of the center screen).

- Press [A]. Your Tyros will now display the Library Load screen.

- Select the desired voices by pressing the button next to the filename you wish to load. (If your USB storage device is not displayed, use the [TAB] buttons to select it.)

- Press [F] to load the file.

Note: If your purchase includes non-Voice data such as Styles, Registrations, Multi Pads and Songs, access them by selecting the type of file you wish to use and going to the USB tab.

#### The 5 steps

#### 1. Update

Make sure your keyboard is up to date and has enough memory to hold the new voices.

#### Tyros4

To load Premium Packs and Voices on your Tyros4, you'll need to have additional flash memory installed. To add flash memory, you will need to install a Yamaha Flash Memory Expansion Module. The two compatible modules for the Tyros4, the FL512M and FL1024M, are both available from Yamaha keyboard retailers. For more information, visit the official Tyros4 website.

#### Tyros3

To load Premium Packs and Voices on your Tyros3, you'll need to have the latest firmware installed, as well as additional RAM. It is recommended that you install two 512 MB expansion memory DIMMs for optimal performance.

#### 2. Purchase

Buy the packs and voices you want from Yamaha MusicSoft.

#### 3. Authenticate

Electronically authorize your instrument to use the packs and voices you've purchased.

Export and upload your Tyros3 or Tyros4's instrument ID, then download and import a license key to authorize your instrument to use the packs and voices you've purchased.

#### 4. Download

Download the voices and packs, then unzip them on your computer.

#### 5. Install

Transfer the voices and packs from your computer to your instrument, load them and start playing!

Transfer the packs and voices from your computer to your instrument using a USB flash drive, then load them or install them permanently on your Tyros3 or Tyros4. You can also transfer the packs and voices to the Tyros3 using a USB cable connection.

Purchase Premium Packs & Voices:

#### Premium Packs

NEW! Vintage Synth
Entertainer
Vintage Keyboard
Euro & US Organ
Choir & Vocals

#### Premium Voices

SA2 Baritone Saxophones
SA2 Female Vocals
SA2 Tenor Saxophones
SA2 Alto Saxophones
SA2 Pan Flutes
SA2 Trombone